# POE
## Manufacturers
https://silvertel.com/poe-power-over-ethernet-html/	Silvertel	POE modules
https://www.st.com/en/power-management/power-over-ethernet-ics/products.html	ST	POE ic's

## Theory
https://www.newnets.ru/knowledge/19942/
IEEE802.3af	up to 13W
IEEE802.3at	up to 30W
IEEE802.3bt	up to 99W

In Power over Ethernet systems, the power sourcing equipment (PSE) senses the Ethernet connection to detect if the powered device (PD) is plugged into the cable termination by applying a small voltage (2.7 V to 10 V) on the Ethernet cable and measures the equivalent resistance in at least two consecutive steps. During this phase, the PD must present a resistance between 23.75 kW and 26.25 kΩ.
Designers can set the current by changing the value of the external resistor according to the following table:
Table 7: Value of the external classification resistor for the different PD classes of power
Class	PD max. average power (W)	RCLS (Ω)
0	13	2k
1	3.84	150
2	6.49	80.6
3	13	51.1
4	25.5	35.6

## PSE - power sourcing equipment
https://www.promelec.ru/fs/sources/87/c4/23/4f/aadba2afb62c992aec11755c.pdf	TI	TPS2384	ic	IEEE 802.3af
https://www.promelec.ru/fs/sources/33/34/f0/a0/1826c683f0397e2116244dbc.pdf	TI	TPS23861PWR	ic	IEEE 802.3at

## PD - powered device

https://www.st.com/en/power-management/pm8800.html	ST	PM8800 (NRND)	ic	IEEE 802.3af	cntrl+dcdc	~5$	https://sds.compel.ru/infosheet/ST/PM8800A
https://www.st.com/en/power-management/pm8803.html	ST	PM8803	ic	IEEE 802.3at	cntrl+dcdc
https://www.st.com/en/power-management/pm8804.html	ST	PM8804	ic		dcdc	~2$	https://sds.compel.ru/infosheet/ST/PM8804TR
https://www.st.com/en/power-management/pm8805.html	ST	PM8805	ic	IEEE 802.3bt	cntrl+dcdc	~15$	https://sds.compel.ru/infosheet/ST/PM8805TR
https://www.promelec.ru/fs/sources/83/5a/32/b8/4aa6318fe63f3c434997a44a.pdf	Onsemi	NCP1083DEG	ic	IEEE 802.3at	cntrl+dcdc
https://www.promelec.ru/fs/sources/99/73/28/c4/81554551ced07229887e94b9.pdf	Onsemi	NCP1081DEG	ic	IEEE 802.3at	cntrl+dcdc
https://www.promelec.ru/fs/sources/99/73/28/c4/81554551ced07229887e94b9.pdf	Onsemi	NCP1081DER2G	ic	IEEE 802.3at	cntrl+dcdc
https://www.promelec.ru/fs/sources/52/ae/5c/b2/34ac659b56d34dfd4922d7ae.pdf	TI	TPS2378	ic	IEEE 802.3at	cntrl+dcdc
https://www.promelec.ru/fs/sources/c2/e0/cb/cb/e2fbf73ad08819189ab1b9d1.pdf	TI	LM5071	ic	IEEE 802.3af	cntrl+dcdc
https://www.promelec.ru/fs/sources/09/d5/e8/fe/a2c6b7a2615d3e8b60dc487b.pdf	TI	TPS2375PW-1	ic	IEEE 802.3af	cntrl
https://www.promelec.ru/fs/sources/a2/6a/5d/af/13f4b6872bf0a775ce680d29.pdf	TI	TPS2375-77	ic	IEEE 802.3af	cntrl
https://www.promelec.ru/fs/sources/f0/74/71/ae/1e7b589d8cfe69839e0f7998.pdf	TI	TPS23750PWPR	ic	IEEE 802.3af	cntrl+dcdc
https://www.promelec.ru/fs/sources/f4/3e/4a/52/ecbe724dd066c62e7ff18afb.pdf	TI	LM5072MHX-80	ic	IEEE 802.3af	cntrl+dcdc