# SIM card
https://en.wikipedia.org/wiki/SIM_card
From left, full-size SIM (1FF), mini-SIM (2FF), micro-SIM (3FF), and nano-SIM (4FF)

SIM card format	Introduced	Standard reference	Length	Width	Thickness
Full-size (1FF)	1991	ISO/IEC 7810:2003, ID-1	85.6 mm (3.37 in)	53.98 mm (2.125 in)	0.76 mm (0.030 in)
Mini-SIM (2FF)	1996	ISO/IEC 7810:2003, ID-000	25 mm (0.98 in)	15 mm (0.59 in)	0.76 mm (0.030 in)
Micro-SIM (3FF)	2003	ETSI TS 102 221 V9.0.0, Mini-UICC	15 mm (0.59 in)	12 mm (0.47 in)	0.76 mm (0.030 in)
Nano-SIM (4FF)	early 2012	ETSI TS 102 221 V11.0.0	12.3 mm (0.48 in)	8.8 mm (0.35 in)	0.67 mm (0.026 in)
Embedded-SIM (eSIM)	2016	ETSI TS 102.671 V9.0.0 JEDEC Design Guide 4.8, SON-8 GSMA SGP.22 V1.0	—	—	—

PUSH-PUSH	with ejection mechanizm
PUSH-PULL	no ejection mechanizm
HINGE	no ejection mechanizm
GUIDE AND HOLDER

At first we need to understand SIM Pinouts:
- 6-pin includes VCC, GND, I/O, VPP, RST, CLK
- 8-pin includes VCC, GND, I/O, VPP, RST, CLK, SIM_PRESENCE, GND
Contact No	Assignment	Description
C1	VCC	Power Voltage.
C2	RST	Reset Signal.
C3	CLK	Clocking Signal.
C4	RFU	Reserved for Feature Use.
C5	GND	Power and Signal Ground.
C6	VPP	Programming Voltage.
C7	I/O	Serial Data input/output.
C8	RFU	Reserved for Feature Use

## ESD
## Power
## Connectors